## Slide 1: Hardware Programming HWP1
capturing a
FPGA
design with
VHDL

## Slide 2: Planning: theory
Third week
  Combinational versus sequential design
  Concurrent and sequential code
  Signals and variables
Fourth week
  Components
  Generics
Fifth week
  Designing state machines
First week
  Introduction digital systems
  Introduction to FPGAs
  Structured digital Design
  Modelling concepts in VHDL
Second week
  Introduction VHDL
  Design verification
  Code structure and data types

## Slide 3: Agenda
Discussion of previous week
Combinational versus sequential design
Concurrent and sequential code
Signals versus variables

## Slide 4
Zie ook:
TABEL:
H.3 ; blz 76

## Slide 5: Agenda
Discussion of previous week
Combinational versus sequential design
Concurrent and sequential code
Signals versus variables

## Slide 6: Combinational and sequential logic (1/2)
Combinational: no memory
The output is a function only of the current inputs.
In any implementation there is a propagation delay
  For this course, we don’t consider the propagation delay.

## Slide 7: Combinational and sequential logic (2/2)
Sequential logic:
The output of sequential logic, is ...
... a function of a sequence of operations ..
... on current and/or previous inputs.
Advantages?
Notes: geheugen
Complexere systemen

## Slide 8: Combinational vs. sequential logic example
R
CLK
D
Q
Combinational
Sequential
A
B
Y
D
Q
R
A
B
Y
Updates instantly as input changes (in theory).
Updates only when CLK goes high. Until then it remembers the previous input (memory)

## Slide 9: Combinational or sequential?
Multiplexer vs. Synchronized Multiplexer?
Timer?
Encoder (for example binary to 7-seg display)?
Comparators?
Adder?
Multiplier?
ALU?
CPU?
Register?
Notes: Multiplexer vs. Gated-Multiplexer -> wat is gated multiplexer? (Combinational)
Timer? (Sequential)
Encoder (for example binary to 7-seg display)? (Combinational)
Comparators? (Combinational)
Adder? (C)
Multiplier? (Combinational)
ALU? (C)
CPU? (Sequential)

## Slide 10: Agenda
Discussion of previous week
Combinational versus sequential design
Concurrent and sequential code
Signals versus variables

## Slide 11: Concurrent Code
concurrent code is intended only for combinational circuits.
  often used for structural descriptions of a circuit.
outputs activated asynchronously, at any time.
statements for concurrent code:
  when ... else
  with ... select
  generate
can be placed outside process, function and procedure

## Slide 12: WITH/SELECT
with ... select is used very often
read: depending on sel, y becomes a when sel is 00, y becomes b when sel is 01, etc…
note the usage of the others keyword here to cover all possibilities
MUX
abcd
Y
sel(1..0)
architecture mux2 of mux is
begin
with sel select
y <= a when "00", -- use "," not ";"
b when "01",
c when "10",
d when others;
end mux2;

## Slide 13: WHEN/ELSE
MUX
abcd
Y
sel(1..0)
architecture mux1 of mux is
begin
y <= a when sel="00" else
b when sel="01" else
c when sel="10" else
d;
end mux1;
Read: when sel is equal to “00”, y obtains the value of a, else when sel is equal to “01”, y obtains the value of b, etc…
Cover all combinations
Let the synthesizer do the K-map for us!
Lijkt op een priority encoder
Notes: Priority encoder -> Interrupt controller bijvoorbeeld.

## Slide 14: Difference
When/Else
With/Select

## Slide 15: Synchronized Multiplexer
library ieee;
use ieee.std_logic_1164.all;
---------------------------------------------
entity synced_mux is
port (a, b, c, d, clk: in std_logic;
sel : in std_logic_vector (1 downto 0);
y : out std_logic);
end gated_mux;
--------------------------------------------
architecture behavioral of synced_mux is
signal x: std_logic;
begin
with sel select
x <= a when "00", -- use "," not ";"
b when "01",
c when "10",
d when others;
process (clk)
begin
if rising_edge(clk) then
y <= x;
end process
end architecture
MUX
abcd
x
sel(1..0)
y
D
Q
DFF
clk

## Slide 16: Sequential Code
statements for sequential code:
  if
  wait
  loop
  case
sequential code can be used to design both sequential and combinational circuits
code within a process, function or procedure is sequential.

## Slide 17: Sequential Code
process is a sequential section, located in the architecture
note that multiple processes are allowed. they are concurrent to each other.
support for the following sequential statements:
  if
  wait
  loop
  case
  with (since 2008)
  when (since 2008)

## Slide 18: Sequential Code Circuit Examples
MUX
A
B
C
D
Y
SEL(1..0)

## Slide 19: Multiplexer with sequential code
A process has a sensitivity list
The outputs of the process get updated if the value of an object in the list changes
MUX
A
B
C
D
Y
SEL(1..0)
library ieee;
use ieee.std_logic_1164.all;
---------------------------------------------
entity seq_code_mux is
port (a, b, c, d: in std_logic;
sel : in std_logic_vector (1 downto 0);
y : out std_logic);
end seq_code_mux;
---------------------------------------------
architecture seq_code_impl of seq_code_mux is
begin
process(sel,a,b,c,d)
begin
if sel = "00" then
y <= a;
elsif sel = "01" then
y <= b;
elsif sel = "10" then
y <= c;
else
y <= d;
end if;
end process;
end seq_code_impl;

## Slide 20: Multiplexer with CASE
library ieee;
use ieee.std_logic_1164.all;
---------------------------------------------
entity seq_code_mux is
port (a, b, c, d: in std_logic;
sel : in std_logic_vector (1 downto 0);
y : out std_logic);
end seq_code_mux;
---------------------------------------------
architecture seq_code_impl of seq_code_mux is
begin
process(sel,a,b,c,d)
begin
case sel is
when "00" =>
y <= a;
when "01" =>
y <= b;
when "10" =>
y <= c;
when others =>
y <= d;
end case;
end process;
end seq_code_impl;

## Slide 21: Difference
Case
If/Else

## Slide 22: Tech. map of mux with sequential code
Sequential Code can make Combinational Circuits
Notes: Uitbreiden.

## Slide 23: D Flip-Flop
library ieee;
use ieee.std_logic_1164.all;
---------------------------------------------
entity dff_example is
port (
clk: in std_logic;
d,r: in std_logic;
q : out std_logic
);
end dff_example;
---------------------------------------------
architecture dff_implementation of dff_example is
begin
process(clk, r )
begin
if r = '1' then
q <= '0';
elsif rising_edge(clk) then
q <= d;
end if;
end process;
end dff_implementation;
D
DFF
Q
R
We only want to update Q when the CLK goes high, so only the CLK & R are in the sensitivity list
Notes: Asynchroon zit onderop: Nieuw Plaatje. Boek
Check de code. Boek p. 287

## Slide 24: Technology Map of DFF
Sequential circuits can only be written with sequential code

## Slide 25: Up/down counter
library ieee;
use ieee.std_logic_1164.all;
use ieee.numeric_std.all;
entity updown is
generic (
counter_width : integer := 31
);
port (
clk : in std_ulogic;
rst : in std_ulogic;
up_ndown : in std_ulogic;
count_out : out std_ulogic_vector(counter_width downto 0)
);
end updown;

## Slide 26: Up/down counter
architecture arch of updown is
variable count : unsigned(counter_width downto 0);
begin
process(clk)
begin
if rising_edge(clk) then
if rst = '1' then
count <= (others => '0');
else
if up_ndown = '1' then
count <= count + 1;
else
count <= count - 1;
end if;
end if;
end if;
end process;
count_out <= std_ulogic_vector(count);
end arch;
Notes: Code klopt niet.

## Slide 27: WAIT
In a process you can use the wait keyword
A process CANNOT have both a sensitivity list and wait statements
Three types:
  wait until condition
  wait on sig1, sig2, ..., sign (sensitivity list)
  wait for time
wait for cannot be synthesized; only for simulation and test benches

## Slide 28: D Flip-Flop with WAIT
LIBRARY ieee;
USE ieee.std_logic_1164.all;
---------------------------------------------
ENTITY dff_example IS
PORT (
clk: IN STD_LOGIC;
d,r: IN STD_LOGIC;
q : OUT STD_LOGIC
);
END dff_example;
---------------------------------------------
ARCHITECTURE dff_implementation OF dff_example IS
BEGIN
PROCESS
BEGIN
WAIT UNTIL RISING_EDGE(clk);
q <= d;
END PROCESS;
END dff_implementation;
Not very handy without a reset 
Notes: Niet per se nuttig of nodig, sensitivity list is beter.

## Slide 29: Loops in VHDL
for and while loops
for ... loop repeats until the upperbound is reached
static bounds; use constants to specify the upper bound of your loop
process(sel)
..
begin
for i in 0 to 5 loop
x <= i;
end loop;
end process;

## Slide 30: Loops in VHDL
while ... loop is similar in structure as the for ... loop
see page 161 of your book for some examples with loops
process(sel)
..
begin
while i<10 loop
...do something...
end loop;
end process;

## Slide 31: Agenda
Discussion of previous week
Combinational versus sequential design
Concurrent and sequential code
Signals versus variables

## Slide 32: Signals versus variables
SIGNAL
  Is eigenlijk een verbinding of draadje
  Bedoeld om data over te brengen tussen verschillende blokken zoals concurrent statements en processen
VARIABLE
  Is meer een abstracte waarde
  Het wordt gebruikt om iets te onthouden binnen een process

## Slide 33: Signals versus variables
SIGNAL properties:
  Can ONLY be declared outside a process but can be used within a process
  Within sequential code the signal is not ‘updated immediately’ (at the end of the process)
  Only a single assignment is allowed to a signal in the whole code (multiple assignments in processes are fine, but only the last one will be effective!)
VARIABLE properties:
  Can ONLY be declared inside a process
  Is ‘updated immediately’ and can be used in the next line of code
  Multiple assignments are not a problem

## Slide 34: Signals and Variables in VHDL (1/2)
library ieee;
use ieee.std_logic_1164.all;
use ieee.numeric_std.all;
entity example is
port (
clk: in std_logic;
x: in std_logic;
counter_a: out integer range 0 to 15;
counter_b: out integer range 0 to 15;
);
end example;
Notes: Geen integer in output

## Slide 35: Signals and Variables in VHDL (2/2)
architecture example of example is
signal a: integer range 0 to 15 := 0;
begin
process (clk)
variable b: integer range 0 to 15 := 0;
begin
if rising_edge(clk) then
a <= a + 1;
b := b + 1;
if x = '1' then
a <= a + 1;
b := b + 1;
end if;
end if;
counter_b <= b;
end process;
counter_a <= a;
end example;
Variable can only be used inside the process!

## Slide 36: Example
When x is high
  The variable counter is counted up twice
  The signal counter is counted up only once
    Only the last assignment is effective for a signal

## Slide 37: Last signal assignment is only used
Proof:
  change a <= a + 1
  to a <= a + 3
Conclusion
  Variables are useful when you have to do multiple assignments inside a process
if rising_edge(clk) then
a <= a + 1;
b := b + 1;
if x = '1' then
a <= a + 3;
b := b + 1;
end if;
end if;
Formally:
<= is a concurrent statement!
:= is a sequential statement!

## Slide 38: Summary
Combinational versus sequential design: no memory versus memory.
In VHDL we can model combinational circuits with sequential statements
Remember the differences between signals and variables

## Slide 39: Homework
Covered today:
  Discussion of previous week
  Combinatorial versus sequential design
  Concurrent and sequential design
  Signals versus variables
Next week:
  Chapter 6 “Code Structure and Composition”