## Slide 1: Hardware Programming HWP1
capturing a
FPGA
design with
VHDL

## Slide 2: Planning: theory
Third week
  Combinational versus sequential design
  Concurrent and sequential code
  Signals and variables
Fourth week
  Components
  Generics
Fifth week
  Designing state machines
First week
  Introduction digital systems
  Introduction to FPGAs
  Structured digital Design
  Modelling concepts in VHDL
Second week
  Introduction VHDL
  Design verification
  Code structure and data types

## Slide 3: Agenda
Discussion of previous week
Component instantiating
Generics

## Slide 4: Signals versus variables
SIGNAL properties:
  Can ONLY be declared outside a PROCESS but can be used within a PROCESS
  Within sequential code the signal is not ‘updated immediately’ (at the end of the PROCESS)
  Only a single assignment is allowed to a signal in the whole code (multiple assignments in PROCESSES are fine, but only the last one will be effective!)
VARIABLE properties:
  Can ONLY be declared inside a PROCESS
  Is ‘updated immediately’ and can be used in the next line of code
  Multiple assignments are not a problem

## Slide 5: Agenda
Discussion of previous week
Component instantiating
Generics

## Slide 6: Putting it together

## Slide 7: Create (separately) validated components
Entity
Architecture
Entity
Architecture

## Slide 8: Add components to your top level design
“ Top Level Design: multiply_2hexandDisplay.vhd”
Notes: Generate
Packages -> demo
Clock toevoegen

## Slide 9: Instantiating components

## Slide 10: Agenda
Discussion of previous week
Component instantiating
Generics

## Slide 11: Generic statements
Generic values are used for declaring global constants in a component
What is the use of generics?
For more information on generics and what else they are capable of, see CH 6.7

## Slide 12: Voorbeeld Generics
With value
Without value
Notes: Dit moet aangepast. Laat ook zien hoe generic map gebruikt wordt.

## Slide 13: Summary
Remember the differences between signals and variables
Components are pre-validated VHDL library elements used to reduce development time of new products.
Next week:
  Chapter 15 (16) “The Case of State Machines